Value	Bits 15 to 8 / hex address	Bits 7 to 0 / hex address	Number of bits used	Divisor (resulting unit)	Other notes
X acceleration	3B	3C	16	8192(g)	Set reg 0x1C, 28 in notes, for ±4g
Y acceleration	3D	3E	16	8192(g)
Z acceleration	3F	40	16	8192(g)

X gyroscope	43	44	16	65.5(°/s)	Set reg 0x1B, 27 in notes, for ± 500°/s
Y gyroscope	45	46	16	65.5(°/s)
Z gyroscope	47	48	16	65.5(°/s)

Register hex number	Register	Value to set hex (binary)	Purpose
1C	Accelerometer config.	0x08 (000 01 000)	Set accelerometer range to ± 4g
19	Sample rate divisor	?
1B	Gyroscope config	0x08 (000 01 000)	Set gyroscope range to ± 500°/s